## Slide 1: רשתות תקשורת 1 מבוא
הקורס מבוסס על הספר:
Computer Networking: A Top-Down Approach 9th edition Jim Kurose, Keith Ross

## Slide 2: רשת האינטרנט
הרשת מכילה:
התקני חישוב
תחנות קצה
שרת לקוח, P2P
IoT
מתגים switches
נתבים routers
קווי תקשורת
fiber, copper
radio, satellite
רשת (ענן) אוסף של התקנים, נתבים, וקווי תקשורת.

## Slide 3: מרכז נתונים (חוות שרתים) - Data Center
רוב הגלישה באינטרנט היא לשרתים של ספקי תוכן Content Providers – Google, Facebook, Netflix
השרתים ממוקמים במרכזי נתונים שמכילים אלפי שרתים.
Google הקימה מעל 30 מרכזי נתונים ברחבי העולם.
מרכזי הנתונים מחוברים ביניהם, התוכן נשמר בכמה מרכזים ומסופק מהקרוב.
מרכזי הנתונים משמשים גם לאחסון שרתים בענן.

## Slide 4: איך לחבר את ספקי שרות האינטרנט - ISP
משתמשי הקצה מחוברים לאינטרנט באמצעות ספקי שרות אינטרנט - ISP
גם מרכזי הנתונים מחוברים ל- ISP
בעיה: כדי שכל מחשב באינטרנט יוכל לגשת לכל מחשב, יש צורך לחבר את כל מיליוני ה- ISP ביניהם
זה דורש N2 חיבורים!
(a) Fully interconnected network. (b) Centralized switch. (c) Two-level hierarchy

## Slide 5: מבנה האינטרנט הוא רשת של רשתות
ISP A
ISP C
ISP B
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
IXP
IXP
access
net
access
net
access
net
access
net
access
net
Content provider network
regional ISP
פתרון: מבנה האינטרנט הוא היררכי
ספק האינטרנט מחובר לספק אזורי
הספקים האזוריים מחוברים למספר מצומצם של ספקים עולמיים
תקשורת בין משתמשי קצה שמחוברים לאותו ISP, תעשה באמצעות אותו ISP
לספקי תוכן יש רשת משלהם

## Slide 6: פרוטוקול
פרוטוקול מגדיר את הפורמט והסדר של ההודעות המועברות בתקשורת, וכן את הפעולה המתבצעת מהעברת ההודעה.
לדוגמה, אם ההודעה מכילה בנוסף לתוכן, את כתובת השולח וכתובת המקבל, כל חלק חייב להיות במקום מסוים ובפורמט מסוים.

## Slide 7: מודל השכבות
Internet
controlled
by OS
controlled by
app developer
transport
application
physical
link
network
process
transport
application
physical
link
network
process
socket
כדי לפשט את המבנה של רשת תקשורת מחלקים אותה לחלקים הנקראים שכבות.
כל שכבה מממשת שרות, ומספקת את השרות באמצעות ממשק מוגדר לשכבה שמעליה (ולכן החלקים נקראים שכבות).
בדומה למחלקה בתכנות מונחה עצמים, אפשר להחליף מימוש של שכבה בלי לשנות את יתר השכבות.
ישנו מודל המחלק את מבנה הרשת לשבע שכבות אך את רשת האינטרנט מקובל לחלק לחמש שכבות

## Slide 8: מודל חמש השכבות של רשת האיטרנט
application: supporting network applications
  HTTP, IMAP, SMTP, DNS
transport: process-process data transfer
  TCP, UDP
network: routing of packets from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi)
physical: bits on the wire
link
application
network
transport
physical
application
transport
network
link
physical

## Slide 9: Encapsulation
source
application
transport
network
link
physical
destination
application
transport
network
link
physical
M
Ht
Hn
Hl
M
Ht
Hn
Ht
M
M
M
message
Ht
M
segment
M
Ht
Hn
packet
frame
M
Ht
Hn
Hl
- כימוס, עיטוףEncapsulation

## Slide 10: Transport layer Encapsulation
source
Transport layer protocol encapsulates application-layer message, M, with transport-layer header Ht to create a transport-layer segment
Ht used by transport layer protocol to implement its service
Transport-layer protocol transfers M (e.g., reliably) from one process to another, using services of network layer
application
transport
network
link
physical
destination
application
transport
network
link
physical
Ht
M
Application exchanges messages to implement some application using services of transport layer
M

## Slide 11: Network layer Encapsulation
source
Ht
M
Network layer protocol encapsulates transport-layer segment [Ht | M] with network layer-layer header Hn to create a network-layer packet
Hn used by network layer protocol to implement its service
Network-layer protocol transfers network -layer packet [Hn |Ht | M] from one host to another, using link layer services
application
transport
network
link
physical
destination
M
application
transport
network
link
physical
M
Ht
Hn

## Slide 12: Link layer Encapsulation
source
Ht
M
link-layer protocol encapsulates network datagram [Hn| [Ht |M], with link-layer header Hl to create a link-layer frame
Link layer protocol transfers frame
[Hl |Hn| [Ht |M] from host to neighboring
host, using physical-layer
application
transport
network
link
physical
destination
M
application
transport
network
link
physical
M
Ht
Hn
M
Ht
Hn
Hl
M
Ht
Hn

## Slide 13: Encapsulation: an end-end view
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
source
Ht
Hn
M
segment
Ht
packet
destination
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame
link
physical

## Slide 14: הנתונים הנשלחים ברשת מחולקים למנות - packets עִקוב במשלוח המנה -packet transmission delay
host sending function:
takes application message
breaks into smaller chunks, known as packets, of length L bits
transmits packet into access network at transmission rate R
R: link transmission rate
host
1
2
two packets,
L bits each
packet
transmission
delay
time needed to
transmit L-bit
packet into link
L (bits)
R (bits/sec)
=
=

## Slide 15: עִקוב במשלוח המנה -packet transmission delay דוגמאות
At time L/R seconds, the source has transmitted the entire packet.
The router can begin to transmit the packet onto the outbound link.
At time 2L/R, the router has transmitted the entire packet.
Thus, the total delay is 2L/R.
The amount of time, until the destination has received the first packet:

## Slide 16: עִקוב במשלוח המנה -packet transmission delay דוגמאות
At time L/R, the router begins to forward the first packet.
But also at time L/R the source will begin to send the second packet.
At time 2L/R, the destination has received the first packet
and the router has received the second packet.
Thus, at time 4L/R the destination has received all three packets.
The amount of time, until the destination has received all three packets:
In general, sending a packet over N links each of rate R
(thus, there are N-1 routers between source and destination).
the end-to-end delay is:

## Slide 17: המנות עוברות באמצעות נתבים מהשולח למקבל הנתב מבצע מיתוג מנות – packet switching
1
2
3
0111
destination address in arriving
packet’s header
routing algorithm
header value
output link
0100
0101
0111
1001
3
2
2
1
local forwarding table
2. Forwarding:
move (switch) arriving packets from router’s input link to appropriate router output link
local forwarding table
1. Routing:
determine source-destination paths taken by packets
routing algorithms
different packet may take different routes
routing algorithm

## Slide 18: Packet-switching: store-and-forward
store and forward: entire packet must arrive at router before it can be transmitted on next link
packet transmission delay: takes L/R seconds to transmit (push out) L-bit packet into link at R bps
source
R bps
destination
1
2
3
L bits
per packet
R bps
One-hop numerical example:
L = 10 Kbits
R = 100 Mbps
one-hop transmission delay = 0.1 msec

## Slide 19: Alternative to packet switching: circuit switching
end-end resources allocated to, reserved for “call” between source and destination
in diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
commonly used in traditional telephone networks

## Slide 20: Packet switching versus circuit switching
example:
1 Gb/s link
each user:
  100 Mb/s when “active”
  active 10% of time
Q: how many users can use this network under circuit-switching and packet switching?
circuit-switching: 10 users
packet switching: with 35 users, probability > 10 active at same time is very small
N
users
1 Gbps link
…..
circuit-switching: Path of Data - Sequential along one fixed path
Bandwidth Use – Fixed guaranteed bandwidth
Latency - Low and predictable
packet-switching: Path of Data - Independent paths; may arrive out of order
Bandwidth Use - Dynamic and shared
Latency - Variable ,depends on network congestion

## Slide 21: queueing delay עִקוב במשלוח המנה -
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for transmission over output link
Queueing occurs when work arrives faster than it can be serviced:
Packet queuing and loss: if arrival rate (in bps) to link exceeds transmission rate (bps) of link for some period of time:
packets will queue in output buffer, waiting to be transmitted on output link
packets can be dropped (lost) if memory (buffer) in router fills up

## Slide 22: packet delay may cause packet loss
packets queue in router buffers, waiting for turn for transmission
  queue length grows when arrival rate to link (temporarily) exceeds output link capacity
packet loss occurs when memory to hold queued packets fills up
A
B
packet being transmitted (transmission delay)
packets in buffers (queueing delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 23: Packet queueing delay (revisited)
a: average packet arrival rate
L: packet length (bits)
R: link bandwidth (bit transmission rate)
La/R ~ 0: avg. queueing delay small
La/R <= 1: avg. queueing delay large
La/R > 1: more “work” arriving is more than can be serviced - average delay infinite!
La/R ~ 0
La/R -> 1
traffic intensity = La/R
average queueing delay
1
service rate of bits
R
arrival rate of bits
L
a
.
:
“traffic
intensity”

## Slide 24: Packet delay: four sources
propagation
processing
queueing
d = dproc + dqueue + dtrans + dprop
A
B
transmission
dtrans: transmission delay:
L: packet length (bits)
R: link transmission rate (bps)
dtrans = L/R
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router

## Slide 25: Packet delay: four sources
dproc: processing
check bit errors
determine output link
typically < microsecs
propagation
processing
queueing
d = dproc + dqueue + dtrans + dprop
A
B
transmission
dprop: propagation delay:
d: length of physical link
s: propagation speed (~2x108 m/sec)
dprop = d/s

## Slide 26: Throughput
throughput: rate (bits/time unit) at which bits are being sent from sender to receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
(Rs bits/sec)
pipe that can carry
fluid at rate
(Rc bits/sec)

## Slide 27: Throughput
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 28: Throughput: network scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck

## Slide 29: “Real” Internet delays and routes
what do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
3 probes
3 probes
3 probes
  sends three packets that will reach router i on path towards destination (with time-to-live field value of i)
  router i will return packets to sender
  sender measures time interval between transmission and reply

## Slide 30: Real Internet delays and routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
* Do some traceroutes from exotic countries at www.traceroute.org
* means no response (probe lost, router not replying)
3 delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
3 delay measurements
to border1-rt-fa5-1-0.gw.umass.edu
looks like delays decrease! Why?
trans-oceanic link